## Slide 1: Klucher Model

## Slide 2
#include <iostream>
#include <fstream>
#include<cmath>
using namespace std;
struct time_date {
int tm_sec; // seconds of minutes from 0 to 61
float tm_min; // minutes of hour from 0 to 59
float tm_hour; // hours of day from 0 to 24
int tm_mday; // day of month from 1 to 31
int tm_mon; // month of year from 0 to 11
int tm_year; // year since 1900
int tm_wday; // days since sunday
int tm_yday; // days since January 1st
int tm_isdst; // hours of daylight savings time
};
struct constants{
float A;
float B;
float C;
};
constants val[12]={
{1202, 0.141, 0.103}, {1187, 0.142, 0.104}, {1164, 0.149, 0.109}, {1130, 0.164, 0.120}, {1106, 0.177, 0.130}, {1092, 0.185, 0.137},
{1093, 0.186, 0.138}, {1107, 0.182, 0.134}, {1136, 0.165, 0.121}, {1136, 0.152, 0.111}, {1190, 0.144, 0.106}, {1204, 0.141, 0.103}
};
bool checkYear(int year)
{
if (year % 400 == 0)
return true;
if (year % 100 == 0)
return false;
if (year % 4 == 0)
return true;
return false;
}

## Slide 3
void ashrae(time_date date, time_date time, float lat)
{
float n = 0; //day of the year
float hra = 0; //hour angle
float dec = 0; //declination angle
float tilt = 0; //tilt angle
float azi = 0; //azimuth angle
float cosQ = 0; //angle of incidence of solar radiation
float cosQz = 0; //zenith angle
int interval = 0; //interval of mins for data representation
float F = 0; //correction coefficient
float Ig = 0; //Hourly Global Radiation
float Ib = 0; //Hourly Beam Radiation
float Id = 0; //Hourly Diffused Radiation
float It = 0; //Solar Radiation on Tilted Surface
cout<<"\nEnter the tilt angle : ";
cin>>tilt;
cout<<"\nEnter the azimuth angle : ";
cin>>azi;
ofstream excel;
excel.open("test.csv");
excel << "Year, Latitude, Tilt Angle, Azimuth Angle" << endl;
excel<<date.tm_year<<" ,"<<lat<<" ,"<<tilt<<" ,"<<azi<<endl;
excel<<endl;
//Converting degrees into radian
lat *=3.14159/180;
tilt *=3.14159/180;
azi *=3.14159/180;
cout<<"\nEnter the interval : ";
cin>>interval;

## Slide 4
excel << "n, Time, Hour Angle, Declination, cosQ, cosQz, Ib, Id, Ig, F, It" << endl;
for(date.tm_mon = 1; date.tm_mon<=12; date.tm_mon++)
{
int ctr=0;
switch (date.tm_mon)
{
case 1: ctr=31;
break;
case 2: ctr=28;
break;
case 3: ctr=31;
break;
case 4: ctr=30;
break;
case 5: ctr=31;
break;
case 6: ctr=30;
break;
case 7: ctr=31;
break;
case 8: ctr=31;
break;
case 9: ctr=30;
break;
case 10: ctr=31;
break;
case 11: ctr=30;
break;
case 12: ctr=31;
break;
default: break;
}
date.tm_mday = 1;

## Slide 5
while (date.tm_mday<=ctr)
{
n = date.tm_mday + (date.tm_mon>1)*31 + (date.tm_mon>2)*28 + (date.tm_mon>3)*31 + (date.tm_mon>4)*30 + (date.tm_mon>5)*31 + (date.tm_mon>6)*30 + (date.tm_mon>7)*31 + (date.tm_mon>8)*31 + (date.tm_mon>9)*30 + (date.tm_mon>10)*31 + (date.tm_mon>11)*30;
n = n + (1*(checkYear(date.tm_year) && date.tm_mon>2)); //if the year is leap year
float deg = (360 * (284+n))/365;
deg *= (3.14159/180);
dec = 23.45 * sin(deg);
dec *= 3.14159/180;
for(time.tm_hour = 5 ; time.tm_hour<18; time.tm_hour++)
{
for(time.tm_min = 0; time.tm_min<60; time.tm_min += interval)
{
hra = 15 * (12 - (time.tm_hour + time.tm_min/60));
hra *= 3.14159/180;
cosQ = sin(lat)*(sin(dec)*cos(tilt) + cos(dec)*cos(azi)*cos(hra)*sin(tilt)) + cos(lat)*(cos(dec)*cos(hra)*cos(tilt) - sin(dec)*cos(azi)*sin(tilt)) + cos(dec)*sin(azi)*sin(hra)*sin(tilt);
cosQz = sin(lat)*sin(dec) + cos(lat)*cos(dec)*cos(hra);

## Slide 6
float Ibn;
Ibn = val[(date.tm_mon-1)].A * exp(-val[(date.tm_mon-1)].B/cosQz);
Ib = Ibn * cosQz;
Id = val[(date.tm_mon-1)].C * Ibn;
Ig = Ib + Id;
F = 1 - ((Id/Ig) * (Id/Ig));
int temp = tilt/(3.14159/180); //temp is tilt in degrees
temp = temp/2;
temp *= 3.14159/180;
float sinQz = pow((1 - (cosQz*cosQz)), 0.5);
It = Ib * (cosQ/cosQz) + Id * ((1+cos(temp))/2) * (1 + (F * pow((sin(temp)),3))) * (1 + F * cosQz * cosQz * sinQz * sinQz * sinQz);
hra = hra/(3.14159/180);
excel<<n<<" ,"<<time.tm_hour<<" : "<<time.tm_min<<" ,"<<hra<<" ,"<<dec<<" ,"<<cosQ<<" ,"<<cosQz<<" ,"<<Ib<<" ,"<<Id<<" ,"<<Ig<<" ,"<<F<<" ,"<<It<<endl;
}
}
date.tm_mday++;
}
}
excel.close();
}

## Slide 7
int main()
{
float lat; //latitude
time_date date, time;
cout<<"Enter the Year: ";
cin>>date.tm_year;
cout<<"\nEnter the Latitude in Degrees: ";
cin>>lat;
ashrae(date, time, lat);
return 0;
}